## Slide 1: A Slice of Raspberry Pi

## Slide 2: Class goals
Write a program called piTempLogger.py that
Links services to an LED indicator
Uses a 7 segment display to show more data.
Reads temperature from a sensor
Emails the temperature to yourself

## Slide 3: Python

## Slide 4: Hello world!
Open terminal or command prompt and type in “python”
In python, type in the following:
print "hello world"
Hello World!

## Slide 5: Math and Variables
Set variable by typing in
x = 1
Multiply, divide, add, subtract
* / + -
Print variables by omitting quotes
print x

## Slide 6: Input
Prompts the user to enter text and saves it to a variable
x = raw_input()

## Slide 7: Multi line programs
Type in all commands into a text file using idle
Save said file as program.py
Close out of the python REPL
Open your program by typing in “python program.py”
In a new file
called ‘program.py’

## Slide 8: For loops
For loops count between 2 numbers.
Code in for’s are indented by spaces, and conditions are ended with colons.
for x in range(0, 10): print x print “goodbye”
Again and again
In a new file
called ‘logger.py’

## Slide 9: Ifs
Ifs execute different code depending on a condition.
Code in ifs are indented by spaces, and conditions are ended with colons.
for x in range(0, 10): if x == 2: print(“Hello World”) elif x == 3: print(“Hallo Weld”) else: print(“Hola Mundo”) print “goodbye”
If this, then that
In ‘logger.py’

## Slide 10: While loops
While loops repeat code while a condition is true.
Code in while loops are indented by spaces, and conditions are ended with colons.
x = 0 while x < 10: if x == 2: print(“Hello World”) elif x == 3: print(“Hallo Weld”) else: print(“Hola Mundo”) x = x + 1 print “goodbye”
Déjà vu
In ‘logger.py’

## Slide 11: Challenge
Make a 4 function calculator in python that takes in a number, then an operation (+-*/), and finally an other number. The input ‘12’, then ‘+’, and finally ‘13’ should print 25.
In a new file
called ‘calc.py’

## Slide 12: Calculator solution
x = float(raw_input()) op = raw_input() y = float(raw_input()) if op == '+': n = x + y elif op == '-': n = x - y elif op == '*': n = x * y elif op == ‘/‘: n = x / y print(n)

## Slide 13: GPIO
GPIO, or General Purpose Input/Output port, is your Pi’s gate to the outside world. It can be used to read values for sensors, or activate LEDs or motors. It can be used in python by using the GPIO module. import RPi.GPIO as GPIO

## Slide 14: Blinking an LED
#import GPIO module import RPi.GPIO as GPIO #import time for sleep function import time #initialize GPIO to use Raspberry Pi pinouts GPIO.setmode(GPIO.BOARD) #set pin 7 to output mode GPIO.setup(15, GPIO.OUT) while True: #turn on LED and wait 1 second GPIO.output(15,True) time.sleep(1) #turn off LED and wait 1 second GPIO.output(15,False) time.sleep(1)
In ‘logger.py’

## Slide 15
3v3
GND
GPIO 22

## Slide 16: Input from buttons
#get access to GPIO module import RPi.GPIO as GPIO #set up pins GPIO.setmode(GPIO.BOARD) GPIO.setup(14, GPIO.IN) GPIO.setup(15, GPIO.OUT) #check whether button is pressed and #change LED accordingly while True: button = GPIO.input(14) GPIO.output(15,button)
In ‘logger.py’

## Slide 17
3v3
GND
GPIO 22
GPIO 23

## Slide 18: Challenge
Make a program that blinks the LED while the button is released, and stops blinking when the button is pressed.
In ‘logger.py’

## Slide 19: Blinker solution
#import GPIO module import RPi.GPIO as GPIO #import time for sleep function import time #initialize GPIO to use Raspberry Pi pinouts GPIO.setmode(GPIO.BOARD) #set pin 7 to output mode GPIO.setup(15, GPIO.OUT) GPIO.setup(14, GPIO.IN) while True: button = GPIO.input(14) while button == True: print 'waiting' #turn on LED and wait 1 second GPIO.output(15,True) time.sleep(1)
#turn off LED and wait 1 second GPIO.output(15,False) time.sleep(1)

## Slide 20: 7 segment displays
7 segment displays operate through a custom module called PiSlice
Set display by using PiSlice.display_number import PiSlice PiSlice.init() PiSlice.number = 12345678
In a new file
called ‘temp.py’

## Slide 21
3v3
GND
GPIO 22
GPIO 23
GPIO 27
GPIO 17
GPIO 18

## Slide 22: Challenge
Add up the number of times you press the button and display it on the 7 segment displays incrementing each time you press the button.
In ‘logger.py’

## Slide 23: Counter solution
#import GPIO module and PiSlice module import RPi.GPIO as GPIO import PiSlice #start up 7 segment display PiSlice.init() num = 0 while True: button = GPIO.input(14) while button == 0: button = GPIO.input(14) while button == 1: button = GPIO.input(14) num = num + 1 PiSlice.number = num

## Slide 24: Sensing temperature
import PiSlice PiSlice.init() PiSlice.init_temp() while True: f, c = PiSlice.read_temp() PiSlice.number = f
In ‘temp.py’

## Slide 25
3v3
GND
GPIO 22
GPIO 23
GPIO 4
GPIO 27
GPIO 17
GPIO 18

## Slide 26: Pi in the sky
Getting your Raspberry Pi project online

## Slide 27: Email
Python can send and receive emails using the SMTP protocol.
You can send yourself data logged from the pi over email
Your email address is LetsCodePi@gmail.com
The password is LetsCode

## Slide 28: Sending emails
import smtplib
fromaddr = 'LetsCodePi@gmail.com'
toaddrs = 'to@addr.com'
msg = 'testing'
# Credentials (if needed)
username = 'LetsCodePi@gmail.com'
password = 'LetsCode'
# The actual mail send
server = smtplib.SMTP('smtp.gmail.com:587')
server.ehlo()
server.starttls()
server.ehlo()
server.login(username,password)
server.sendmail(fromaddr, toaddrs, msg)
server.quit()
In a new file
called ‘mail.py’

## Slide 29: Final challenge
Make a program based off of the button counter that can show the number of emails you have and the current room's temperature. Cycle through these modes by pressing the button and display your output on the 7 segment displays.
In ‘logger.py’